## Slide 1
IN403 · Advanced Network Protocols, Architectures & Security
LECTURE 01 · 2 HOURS
TCP/IP Deep Dive I: Reliable Transport & Flow Control
Course kickoff, TCP segment anatomy, connection management and the sliding-window flow-control machinery
Course topic: TCP/IP Deep Dive
Notes: Welcome. This lecture session runs 2 hours. Course kickoff, TCP segment anatomy, connection management and the sliding-window flow-control machinery

## Slide 2
Learning objectives
By the end of this session you will be able to:
1
Explain the course structure, assessment and lab tooling
2
Dissect the TCP header and explain the purpose of every field and key option
3
Trace connection establishment, teardown and the TCP state machine
4
Describe sliding-window flow control, the receive window and window scaling
5
Diagnose zero-window, silly-window syndrome and Nagle/delayed-ACK interactions
IN403 · Lecture 1 · TCP Deep Dive I
2
Notes: Read the objectives aloud and connect each one to the agenda that follows.

## Slide 3
Session plan (120 minutes)
10′
25′
25′
10′
30′
12′
8′
0:00 – 0:10
Course introduction, assessment and tools
0:10 – 0:35
TCP service model and segment anatomy
0:35 – 1:00
Connection management & state machine
1:00 – 1:10
Break
1:10 – 1:40
Flow control: sliding window, scaling, zero window, SWS
1:40 – 1:52
In-class activity: window arithmetic
1:52 – 2:00
Quiz and wrap-up
IN403 · Lecture 1 · TCP Deep Dive I
3
Notes: Timing guide for the 2-hour session, including a 10-minute break. Adjust pacing as needed.

## Slide 4
About IN403
Advanced Network Protocols, Architectures & Security · M1S1 · 5 credits
1
Lectures · 34 h
17 two-hour sessions covering TCP, QoS, NFV, SDN, advanced routing, IPsec/TLS, measurement, QUIC/HTTP/3 and network design.
2
Labs · 16 h
8 two-hour hands-on labs with Wireshark, iPerf3, Linux tc, Mininet + Ryu, FRRouting/GNS3, strongSwan and QUIC tooling.
3
Assessment
Lab reports and practical checks, a mid-term exam after the routing block, and a final written exam. Exact weights are set by the department.
4
References
Kurose & Ross — Computer Networking: A Top-Down Approach · Forouzan — Data Communications and Networking · Goransson & Black — Software Defined Networks.
IN403 · Lecture 1 · TCP Deep Dive I
4
Notes: Present the course logistics. Replace the assessment placeholder text with your institution’s official weights.

## Slide 5
Course roadmap
Transport (L1–L3)
TCP flow control, congestion control (Reno, CUBIC, BBR), performance tuning
QoS (L4–L6)
Shaping and policing, scheduling, IntServ/RSVP, DiffServ
Virtualization (L7–L10)
NFV architecture & MANO, SDN, OpenFlow, controllers
Routing (L11–L12)
Advanced OSPF, BGP for inter-domain routing
Security (L13–L14)
IPsec and TLS protocol flows
Ops & future (L15–L17)
Measurement, QUIC & HTTP/3, network design principles
IN403 · Lecture 1 · TCP Deep Dive I
5
Notes: Show how the blocks build on each other: transport first, then how networks treat traffic, how they are programmed, routed, secured and measured. Explanation for students: The course follows a packet’s life from the end host outwards. We start inside the transport layer (TCP), because almost every later topic — QoS, measurement, QUIC — reacts to how TCP behaves. Next we look at how the network can treat traffic differently (QoS), then at how modern networks are built and programmed in software (NFV and SDN). With that foundation we study how packets find their way between and within organisations (OSPF and BGP), how they are protected (IPsec and TLS), how we measure whether all of this works, and finally where protocols are heading (QUIC, HTTP/3) and how to design a complete network. Each lab is scheduled right after the lectures it supports, so you will always practise a topic within a week or two of seeing it in class.

## Slide 6
Course roadmap
EXPLAINED
The course follows a packet’s life from the end host outwards. We start inside the transport layer (TCP), because almost every later topic — QoS, measurement, QUIC — reacts to how TCP behaves. Next we look at how the network can treat traffic differently (QoS), then at how modern networks are built and programmed in software (NFV and SDN).
With that foundation we study how packets find their way between and within organisations (OSPF and BGP), how they are protected (IPsec and TLS), how we measure whether all of this works, and finally where protocols are heading (QUIC, HTTP/3) and how to design a complete network.
Each lab is scheduled right after the lectures it supports, so you will always practise a topic within a week or two of seeing it in class.
REMEMBER
Every block builds on the previous one. If TCP congestion control is unclear, QoS and QUIC will be harder — revise L1–L3 early.
IN403 · Lecture 1 · TCP Deep Dive I
6
Notes: The course follows a packet’s life from the end host outwards. We start inside the transport layer (TCP), because almost every later topic — QoS, measurement, QUIC — reacts to how TCP behaves. Next we look at how the network can treat traffic differently (QoS), then at how modern networks are built and programmed in software (NFV and SDN). With that foundation we study how packets find their way between and within organisations (OSPF and BGP), how they are protected (IPsec and TLS), how we measure whether all of this works, and finally where protocols are heading (QUIC, HTTP/3) and how to design a complete network. Each lab is scheduled right after the lectures it supports, so you will always practise a topic within a week or two of seeing it in class. Remember: Every block builds on the previous one. If TCP congestion control is unclear, QoS and QUIC will be harder — revise L1–L3 early.

## Slide 7
01
The TCP service model
What TCP promises the application — and what it does not
IN403 · Lecture 1 · TCP Deep Dive I
7

## Slide 8
TCP vs UDP: two transport contracts
TCP
Connection-oriented (3-way handshake)
Reliable, in-order byte stream
Flow control (protects the receiver)
Congestion control (protects the network)
Full-duplex, point-to-point
Used by HTTP/1.1–2, SSH, SMTP, BGP
UDP
Connectionless, no handshake
Best-effort datagrams; may be lost or reordered
No flow or congestion control
Minimal 8-byte header, low latency
Supports multicast/broadcast
Used by DNS, VoIP/RTP, DHCP, QUIC (HTTP/3)
IN403 · Lecture 1 · TCP Deep Dive I
8
Notes: Emphasise that TCP is a byte stream, not a message service. QUIC (Lecture 16) rebuilds TCP-like services on top of UDP. Explanation for students: The transport layer offers applications a service contract. TCP promises that every byte you write will arrive, exactly once and in order, or that you will be told the connection failed. To keep that promise it needs a connection (state at both ends), sequence numbers, acknowledgments and retransmissions. UDP promises almost nothing: each datagram is sent independently and may be lost, duplicated or reordered. In exchange it adds only 8 bytes of header and no set-up delay, which suits short exchanges (DNS) and real-time media where a late packet is as useless as a lost one. An important subtlety is that TCP is a byte stream: if you send two 100-byte messages, the receiver may read 200 bytes at once or 50 bytes at a time. Applications must define their own message boundaries.

## Slide 9
TCP vs UDP: two transport contracts
EXPLAINED
The transport layer offers applications a service contract. TCP promises that every byte you write will arrive, exactly once and in order, or that you will be told the connection failed. To keep that promise it needs a connection (state at both ends), sequence numbers, acknowledgments and retransmissions.
UDP promises almost nothing: each datagram is sent independently and may be lost, duplicated or reordered. In exchange it adds only 8 bytes of header and no set-up delay, which suits short exchanges (DNS) and real-time media where a late packet is as useless as a lost one.
An important subtlety is that TCP is a byte stream: if you send two 100-byte messages, the receiver may read 200 bytes at once or 50 bytes at a time. Applications must define their own message boundaries.
EXAMPLE
A video call uses UDP (RTP): if a voice packet is lost, retransmitting it 100 ms later is pointless. A file download uses TCP: a single missing byte would corrupt the file.
REMEMBER
TCP = reliable ordered byte stream with flow and congestion control. UDP = best-effort datagrams. QUIC rebuilds TCP-like reliability on top of UDP.
IN403 · Lecture 1 · TCP Deep Dive I
9
Notes: The transport layer offers applications a service contract. TCP promises that every byte you write will arrive, exactly once and in order, or that you will be told the connection failed. To keep that promise it needs a connection (state at both ends), sequence numbers, acknowledgments and retransmissions. UDP promises almost nothing: each datagram is sent independently and may be lost, duplicated or reordered. In exchange it adds only 8 bytes of header and no set-up delay, which suits short exchanges (DNS) and real-time media where a late packet is as useless as a lost one. An important subtlety is that TCP is a byte stream: if you send two 100-byte messages, the receiver may read 200 bytes at once or 50 bytes at a time. Applications must define their own message boundaries. Example: A video call uses UDP (RTP): if a voice packet is lost, retransmitting it 100 ms later is pointless. A file download uses TCP: a single missing byte would corrupt the file. Remember: TCP = reliable ordered byte stream with flow and congestion control. UDP = best-effort datagrams. QUIC rebuilds TCP-like reliability on top of UDP.

## Slide 10
TCP header: field by field
Field | Size | Purpose
Source / Destination port | 16 b each | Identify the sending and receiving processes (socket demultiplexing)
Sequence number | 32 b | Byte offset of the first data byte in this segment (random ISN)
Acknowledgment number | 32 b | Next byte expected from the peer — cumulative ACK
Data offset | 4 b | Header length in 32-bit words (20–60 bytes)
Flags | 9 b | CWR, ECE, URG, ACK, PSH, RST, SYN, FIN (+ NS, historic)
Window | 16 b | Receive window advertised to the peer (scaled by option)
Checksum | 16 b | Covers header, data and IP pseudo-header
Urgent pointer / Options | 16 b / var. | Rarely used urgent data; MSS, WScale, SACK, Timestamps
IN403 · Lecture 1 · TCP Deep Dive I
10
Notes: Walk through a real header capture if possible. Stress that sequence numbers count bytes, not segments. Explanation for students: Each TCP segment carries a header of 20 bytes plus up to 40 bytes of options. The port numbers identify the two application processes; together with the two IP addresses they form the 4-tuple that names a connection. The sequence number is the position (in bytes) of the first data byte of this segment in the sender’s stream. The acknowledgment number tells the other side “I have received everything up to this byte; send me this one next”. Because it is cumulative, one ACK can confirm many segments. The flags control the connection: SYN opens it, FIN closes it gracefully, RST aborts it, ACK means the acknowledgment field is valid, PSH asks the receiver to deliver data to the application promptly. The window field is how the receiver says how much more data it can accept — this is the heart of flow control.

## Slide 11
TCP header: field by field
EXPLAINED
Each TCP segment carries a header of 20 bytes plus up to 40 bytes of options. The port numbers identify the two application processes; together with the two IP addresses they form the 4-tuple that names a connection.
The sequence number is the position (in bytes) of the first data byte of this segment in the sender’s stream. The acknowledgment number tells the other side “I have received everything up to this byte; send me this one next”. Because it is cumulative, one ACK can confirm many segments.
The flags control the connection: SYN opens it, FIN closes it gracefully, RST aborts it, ACK means the acknowledgment field is valid, PSH asks the receiver to deliver data to the application promptly. The window field is how the receiver says how much more data it can accept — this is the heart of flow control.
EXAMPLE
A segment with seq = 5001 carrying 1000 bytes contains bytes 5001–6000. The receiver answers with ack = 6001, meaning “next I expect byte 6001”.
REMEMBER
Sequence and ACK numbers count bytes, not packets. The ACK number is always the next byte expected.
IN403 · Lecture 1 · TCP Deep Dive I
11
Notes: Each TCP segment carries a header of 20 bytes plus up to 40 bytes of options. The port numbers identify the two application processes; together with the two IP addresses they form the 4-tuple that names a connection. The sequence number is the position (in bytes) of the first data byte of this segment in the sender’s stream. The acknowledgment number tells the other side “I have received everything up to this byte; send me this one next”. Because it is cumulative, one ACK can confirm many segments. The flags control the connection: SYN opens it, FIN closes it gracefully, RST aborts it, ACK means the acknowledgment field is valid, PSH asks the receiver to deliver data to the application promptly. The window field is how the receiver says how much more data it can accept — this is the heart of flow control. Example: A segment with seq = 5001 carrying 1000 bytes contains bytes 5001–6000. The receiver answers with ack = 6001, meaning “next I expect byte 6001”. Remember: Sequence and ACK numbers count bytes, not packets. The ACK number is always the next byte expected.

## Slide 12
TCP options that matter for performance
M
MSS
Maximum Segment Size, announced in the SYN. Typically 1460 bytes on Ethernet (1500 MTU − 40). Avoids IP fragmentation.
W
Window Scale
Shift count (0–14) applied to the 16-bit window, allowing windows up to 1 GiB. Negotiated only in SYN/SYN-ACK (RFC 7323).
S
SACK
Selective Acknowledgment: receiver reports non-contiguous blocks received, so the sender retransmits only the holes (RFC 2018).
T
Timestamps
TSval/TSecr enable accurate RTT measurement on every ACK and PAWS protection against wrapped sequence numbers (RFC 7323).
IN403 · Lecture 1 · TCP Deep Dive I
12
Notes: These four options are negotiated in the handshake; middleboxes that strip them can quietly destroy performance. Explanation for students: The original TCP header was designed in 1981 for slow links. Options extend it without changing the fixed header. Four options are negotiated in almost every modern connection, and they are only valid if both SYN and SYN-ACK carry them. MSS tells the peer the largest segment you can receive, avoiding IP fragmentation. Window Scale multiplies the 16-bit window field by 2^shift so the window can exceed 64 KB — essential on fast, long paths. SACK lets the receiver report which out-of-order blocks it already has, so only the missing pieces are resent. Timestamps echo a clock value so the sender can measure RTT on every ACK and detect wrapped sequence numbers on very fast links.

## Slide 13
TCP options that matter for performance
EXPLAINED
The original TCP header was designed in 1981 for slow links. Options extend it without changing the fixed header. Four options are negotiated in almost every modern connection, and they are only valid if both SYN and SYN-ACK carry them.
MSS tells the peer the largest segment you can receive, avoiding IP fragmentation. Window Scale multiplies the 16-bit window field by 2^shift so the window can exceed 64 KB — essential on fast, long paths. SACK lets the receiver report which out-of-order blocks it already has, so only the missing pieces are resent. Timestamps echo a clock value so the sender can measure RTT on every ACK and detect wrapped sequence numbers on very fast links.
EXAMPLE
A firewall that strips the Window Scale option silently limits every connection through it to 64 KB in flight. On a 100 ms path that caps throughput at about 5 Mb/s even on a 1 Gb/s link.
REMEMBER
Options are agreed in the handshake and fixed for the whole connection. Check them first when diagnosing slow transfers.
IN403 · Lecture 1 · TCP Deep Dive I
13
Notes: The original TCP header was designed in 1981 for slow links. Options extend it without changing the fixed header. Four options are negotiated in almost every modern connection, and they are only valid if both SYN and SYN-ACK carry them. MSS tells the peer the largest segment you can receive, avoiding IP fragmentation. Window Scale multiplies the 16-bit window field by 2^shift so the window can exceed 64 KB — essential on fast, long paths. SACK lets the receiver report which out-of-order blocks it already has, so only the missing pieces are resent. Timestamps echo a clock value so the sender can measure RTT on every ACK and detect wrapped sequence numbers on very fast links. Example: A firewall that strips the Window Scale option silently limits every connection through it to 64 KB in flight. On a 100 ms path that caps throughput at about 5 Mb/s even on a 1 Gb/s link. Remember: Options are agreed in the handshake and fixed for the whole connection. Check them first when diagnosing slow transfers.

## Slide 14
02
Connection management
Handshake, teardown and the TCP finite state machine
IN403 · Lecture 1 · TCP Deep Dive I
14

## Slide 15
Three-way handshake and option negotiation
Client
Server
SYN seq=x [MSS=1460, WS=7, SACK_PERM, TS]
SYN-ACK seq=y ack=x+1 [MSS, WS=8, SACK_PERM, TS]
ACK seq=x+1 ack=y+1
Data seq=x+1 …
ISNs are randomised to resist spoofing and old-segment confusion
Options are only honoured if both sides offer them
SYN and FIN each consume one sequence number
SYN cookies let a server survive SYN floods without keeping state
IN403 · Lecture 1 · TCP Deep Dive I
15
Notes: Draw attention to the asymmetric window-scale values: each direction has its own shift count. Explanation for students: Before any data flows, both sides must agree on starting sequence numbers and options. The client sends a SYN with its initial sequence number x and its options. The server replies with SYN-ACK: its own initial sequence number y, an acknowledgment of x+1 and its options. The client completes with an ACK of y+1. Why three messages and not two? Each side must prove it received the other’s sequence number. Two messages would leave the server unsure that its SYN reached the client. Initial sequence numbers are random so an attacker cannot guess them and so that segments from an old connection are not mistaken for new ones. Handshake state is a target for attacks: a SYN flood sends many SYNs without completing them, filling the server’s queue. SYN cookies encode the state inside the server’s ISN so nothing must be stored until the final ACK arrives.

## Slide 16
Three-way handshake and option negotiation
EXPLAINED
Before any data flows, both sides must agree on starting sequence numbers and options. The client sends a SYN with its initial sequence number x and its options. The server replies with SYN-ACK: its own initial sequence number y, an acknowledgment of x+1 and its options. The client completes with an ACK of y+1.
Why three messages and not two? Each side must prove it received the other’s sequence number. Two messages would leave the server unsure that its SYN reached the client. Initial sequence numbers are random so an attacker cannot guess them and so that segments from an old connection are not mistaken for new ones.
Handshake state is a target for attacks: a SYN flood sends many SYNs without completing them, filling the server’s queue. SYN cookies encode the state inside the server’s ISN so nothing must be stored until the final ACK arrives.
EXAMPLE
Client SYN seq=1000, server SYN-ACK seq=5000 ack=1001, client ACK seq=1001 ack=5001. The first data byte from the client will be numbered 1001.
REMEMBER
The handshake costs one RTT before data can be sent. Later lectures (TLS 1.3, QUIC) work hard to reduce this cost.
IN403 · Lecture 1 · TCP Deep Dive I
16
Notes: Before any data flows, both sides must agree on starting sequence numbers and options. The client sends a SYN with its initial sequence number x and its options. The server replies with SYN-ACK: its own initial sequence number y, an acknowledgment of x+1 and its options. The client completes with an ACK of y+1. Why three messages and not two? Each side must prove it received the other’s sequence number. Two messages would leave the server unsure that its SYN reached the client. Initial sequence numbers are random so an attacker cannot guess them and so that segments from an old connection are not mistaken for new ones. Handshake state is a target for attacks: a SYN flood sends many SYNs without completing them, filling the server’s queue. SYN cookies encode the state inside the server’s ISN so nothing must be stored until the final ACK arrives. Example: Client SYN seq=1000, server SYN-ACK seq=5000 ack=1001, client ACK seq=1001 ack=5001. The first data byte from the client will be numbered 1001. Remember: The handshake costs one RTT before data can be sent. Later lectures (TLS 1.3, QUIC) work hard to reduce this cost.

## Slide 17
Connection teardown and TIME_WAIT
Active closer
Passive closer
FIN (FIN_WAIT_1)
ACK (CLOSE_WAIT / FIN_WAIT_2)
remaining data …
FIN (LAST_ACK)
ACK → TIME_WAIT for 2×MSL
Each direction is closed independently (half-close)
TIME_WAIT (2×MSL, 60 s on Linux) absorbs late segments and re-sends the final ACK
Busy clients can exhaust ephemeral ports with TIME_WAIT sockets
RST aborts immediately — no graceful shutdown
IN403 · Lecture 1 · TCP Deep Dive I
17
Notes: Ask students why it is the active closer, not the server, that should ideally hold TIME_WAIT. Explanation for students: TCP is full-duplex, so each direction is closed separately. The side that finishes first (the active closer) sends FIN; the other side acknowledges it but may continue sending its own data (a half-close). When it is done, it sends its own FIN, which the active closer acknowledges. After that last ACK the active closer waits in TIME_WAIT for twice the Maximum Segment Lifetime. This serves two purposes: if the final ACK was lost, the peer will resend its FIN and we can answer it; and any delayed duplicate segments from this connection will expire before the same 4-tuple can be reused. RST is different: it aborts the connection immediately and discards any data still in buffers. It is sent, for example, when a segment arrives for a port with no listening application.

## Slide 18
Connection teardown and TIME_WAIT
EXPLAINED
TCP is full-duplex, so each direction is closed separately. The side that finishes first (the active closer) sends FIN; the other side acknowledges it but may continue sending its own data (a half-close). When it is done, it sends its own FIN, which the active closer acknowledges.
After that last ACK the active closer waits in TIME_WAIT for twice the Maximum Segment Lifetime. This serves two purposes: if the final ACK was lost, the peer will resend its FIN and we can answer it; and any delayed duplicate segments from this connection will expire before the same 4-tuple can be reused.
RST is different: it aborts the connection immediately and discards any data still in buffers. It is sent, for example, when a segment arrives for a port with no listening application.
EXAMPLE
A load-testing client opening thousands of short connections per second can run out of local ports because each closed connection keeps its port in TIME_WAIT for 60 seconds (Linux).
REMEMBER
Whoever closes first holds TIME_WAIT. Servers usually prefer clients to close first.
IN403 · Lecture 1 · TCP Deep Dive I
18
Notes: TCP is full-duplex, so each direction is closed separately. The side that finishes first (the active closer) sends FIN; the other side acknowledges it but may continue sending its own data (a half-close). When it is done, it sends its own FIN, which the active closer acknowledges. After that last ACK the active closer waits in TIME_WAIT for twice the Maximum Segment Lifetime. This serves two purposes: if the final ACK was lost, the peer will resend its FIN and we can answer it; and any delayed duplicate segments from this connection will expire before the same 4-tuple can be reused. RST is different: it aborts the connection immediately and discards any data still in buffers. It is sent, for example, when a segment arrives for a port with no listening application. Example: A load-testing client opening thousands of short connections per second can run out of local ports because each closed connection keeps its port in TIME_WAIT for 60 seconds (Linux). Remember: Whoever closes first holds TIME_WAIT. Servers usually prefer clients to close first.

## Slide 19
The TCP state machine in five phases
1
Closed / Listen
Server calls listen(); client is CLOSED until connect().
2
Opening
SYN_SENT on the client, SYN_RECEIVED on the server while the handshake completes.
3
Established
Data transfer in both directions; flow and congestion control are active.
4
Closing
FIN_WAIT_1/2, CLOSE_WAIT, CLOSING, LAST_ACK depending on who closes first.
5
Time-wait
Active closer waits 2×MSL before returning to CLOSED.
IN403 · Lecture 1 · TCP Deep Dive I
19
Notes: Use `ss -tan` on a Linux box to show live sockets in these states. Explanation for students: TCP defines eleven states, but they group naturally into five phases. A server starts in LISTEN; a client moves from CLOSED to SYN_SENT when it calls connect(). During the handshake the server is in SYN_RECEIVED. When the handshake completes, both reach ESTABLISHED, where all data transfer happens. Closing involves several intermediate states depending on who closes first and whether both close at the same time: FIN_WAIT_1 and FIN_WAIT_2 for the active closer, CLOSE_WAIT and LAST_ACK for the passive closer, and the rare CLOSING state for simultaneous close. Finally the active side spends time in TIME_WAIT before returning to CLOSED. Knowing these states is practical: a server with thousands of sockets in CLOSE_WAIT usually means the application is not calling close() — an application bug, not a network problem.

## Slide 20
The TCP state machine in five phases
EXPLAINED
TCP defines eleven states, but they group naturally into five phases. A server starts in LISTEN; a client moves from CLOSED to SYN_SENT when it calls connect(). During the handshake the server is in SYN_RECEIVED. When the handshake completes, both reach ESTABLISHED, where all data transfer happens.
Closing involves several intermediate states depending on who closes first and whether both close at the same time: FIN_WAIT_1 and FIN_WAIT_2 for the active closer, CLOSE_WAIT and LAST_ACK for the passive closer, and the rare CLOSING state for simultaneous close. Finally the active side spends time in TIME_WAIT before returning to CLOSED.
Knowing these states is practical: a server with thousands of sockets in CLOSE_WAIT usually means the application is not calling close() — an application bug, not a network problem.
EXAMPLE
Command: ss -tan state close-wait lists connections the remote side has closed but your application has not yet closed.
REMEMBER
ESTABLISHED = data phase. Many CLOSE_WAIT = app bug. Many TIME_WAIT = many short connections from this host.
IN403 · Lecture 1 · TCP Deep Dive I
20
Notes: TCP defines eleven states, but they group naturally into five phases. A server starts in LISTEN; a client moves from CLOSED to SYN_SENT when it calls connect(). During the handshake the server is in SYN_RECEIVED. When the handshake completes, both reach ESTABLISHED, where all data transfer happens. Closing involves several intermediate states depending on who closes first and whether both close at the same time: FIN_WAIT_1 and FIN_WAIT_2 for the active closer, CLOSE_WAIT and LAST_ACK for the passive closer, and the rare CLOSING state for simultaneous close. Finally the active side spends time in TIME_WAIT before returning to CLOSED. Knowing these states is practical: a server with thousands of sockets in CLOSE_WAIT usually means the application is not calling close() — an application bug, not a network problem. Example: Command: ss -tan state close-wait lists connections the remote side has closed but your application has not yet closed. Remember: ESTABLISHED = data phase. Many CLOSE_WAIT = app bug. Many TIME_WAIT = many short connections from this host.

## Slide 21
03
Flow control
Never let a fast sender overrun a slow receiver
IN403 · Lecture 1 · TCP Deep Dive I
21

## Slide 22
Sliding-window flow control
Receiver buffer: data waits here until the application calls read()
rwnd = free space in the buffer, advertised in every ACK
Sender rule: LastByteSent − LastByteAcked ≤ min(rwnd, cwnd)
Window slides as ACKs arrive
  Left edge advances with cumulative ACKs
  Right edge advances when the app reads data
Throughput bound: Throughput ≤ Window / RTT
=
Worked example
With a 64 KB window and a 100 ms RTT, the maximum throughput is 65 535 × 8 / 0.1 ≈ 5.2 Mb/s — no matter how fast the link is. This is why window scaling exists.
IN403 · Lecture 1 · TCP Deep Dive I
22
Notes: Derive Throughput = W/RTT on the board. Students should leave able to do this calculation quickly. Explanation for students: The receiver stores incoming data in a buffer until the application reads it. If the sender transmitted faster than the application reads, this buffer would overflow and data would be lost. Flow control prevents that: in every segment the receiver advertises rwnd, the free space left in its buffer. The sender may have at most rwnd bytes “in flight” (sent but not yet acknowledged). As acknowledgments arrive the left edge of the window moves forward; as the application reads data the receiver advertises more space and the right edge moves forward. The window therefore slides along the byte stream. Because the sender must wait for ACKs, at most one window of data can be delivered per round-trip time. This gives the fundamental limit: Throughput ≤ Window / RTT. The faster or longer the path, the bigger the window must be.

## Slide 23
Sliding-window flow control
EXPLAINED
The receiver stores incoming data in a buffer until the application reads it. If the sender transmitted faster than the application reads, this buffer would overflow and data would be lost. Flow control prevents that: in every segment the receiver advertises rwnd, the free space left in its buffer.
The sender may have at most rwnd bytes “in flight” (sent but not yet acknowledged). As acknowledgments arrive the left edge of the window moves forward; as the application reads data the receiver advertises more space and the right edge moves forward. The window therefore slides along the byte stream.
Because the sender must wait for ACKs, at most one window of data can be delivered per round-trip time. This gives the fundamental limit: Throughput ≤ Window / RTT. The faster or longer the path, the bigger the window must be.
EXAMPLE
With rwnd = 64 KB and RTT = 100 ms: 65 535 × 8 bits / 0.1 s ≈ 5.2 Mb/s. Doubling the window to 128 KB doubles the maximum throughput to about 10.5 Mb/s.
REMEMBER
The sender obeys min(rwnd, cwnd). rwnd protects the receiver; cwnd (Lecture 2) protects the network.
IN403 · Lecture 1 · TCP Deep Dive I
23
Notes: The receiver stores incoming data in a buffer until the application reads it. If the sender transmitted faster than the application reads, this buffer would overflow and data would be lost. Flow control prevents that: in every segment the receiver advertises rwnd, the free space left in its buffer. The sender may have at most rwnd bytes “in flight” (sent but not yet acknowledged). As acknowledgments arrive the left edge of the window moves forward; as the application reads data the receiver advertises more space and the right edge moves forward. The window therefore slides along the byte stream. Because the sender must wait for ACKs, at most one window of data can be delivered per round-trip time. This gives the fundamental limit: Throughput ≤ Window / RTT. The faster or longer the path, the bigger the window must be. Example: With rwnd = 64 KB and RTT = 100 ms: 65 535 × 8 bits / 0.1 s ≈ 5.2 Mb/s. Doubling the window to 128 KB doubles the maximum throughput to about 10.5 Mb/s. Remember: The sender obeys min(rwnd, cwnd). rwnd protects the receiver; cwnd (Lecture 2) protects the network.

## Slide 24
Sender’s view of the byte stream
Sent & acknowledged
Bytes left of the window — buffer space can be freed
Sent, not yet ACKed
“In flight” — must be kept for possible retransmission
Usable window
Can be sent now without waiting for any ACK
Outside window
Cannot be sent until the window slides right
Window size = in flight + usable
A new ACK moves the left edge; a larger rwnd moves the right edge
If rwnd shrinks to 0 the sender stops and starts the persist timer
IN403 · Lecture 1 · TCP Deep Dive I
24
Notes: Animate this on the board by moving two pointers along a byte line. Explanation for students: Picture the sender’s data as a long line of numbered bytes divided into four regions. On the far left are bytes already sent and acknowledged: the sender can free that buffer space. Next come bytes sent but not yet acknowledged: they must be kept in case they need retransmitting. Then comes the usable window: bytes the sender is allowed to send right now without waiting. Everything to the right is outside the window and must wait. The window size equals the in-flight bytes plus the usable bytes. When an ACK arrives, the boundary between the first two regions moves right and the usable window grows. If the receiver advertises a smaller window, the right edge stops moving; if it advertises zero, the sender stops completely and starts the persist timer.

## Slide 25
Sender’s view of the byte stream
EXPLAINED
Picture the sender’s data as a long line of numbered bytes divided into four regions. On the far left are bytes already sent and acknowledged: the sender can free that buffer space. Next come bytes sent but not yet acknowledged: they must be kept in case they need retransmitting.
Then comes the usable window: bytes the sender is allowed to send right now without waiting. Everything to the right is outside the window and must wait. The window size equals the in-flight bytes plus the usable bytes.
When an ACK arrives, the boundary between the first two regions moves right and the usable window grows. If the receiver advertises a smaller window, the right edge stops moving; if it advertises zero, the sender stops completely and starts the persist timer.
EXAMPLE
Window = 10 000 bytes, 6 000 in flight ⇒ 4 000 usable. An ACK for 3 000 bytes arrives with the same window ⇒ 3 000 in flight and 7 000 usable.
REMEMBER
Window = in flight + usable. ACKs move the left edge; window advertisements move the right edge.
IN403 · Lecture 1 · TCP Deep Dive I
25
Notes: Picture the sender’s data as a long line of numbered bytes divided into four regions. On the far left are bytes already sent and acknowledged: the sender can free that buffer space. Next come bytes sent but not yet acknowledged: they must be kept in case they need retransmitting. Then comes the usable window: bytes the sender is allowed to send right now without waiting. Everything to the right is outside the window and must wait. The window size equals the in-flight bytes plus the usable bytes. When an ACK arrives, the boundary between the first two regions moves right and the usable window grows. If the receiver advertises a smaller window, the right edge stops moving; if it advertises zero, the sender stops completely and starts the persist timer. Example: Window = 10 000 bytes, 6 000 in flight ⇒ 4 000 usable. An ACK for 3 000 bytes arrives with the same window ⇒ 3 000 in flight and 7 000 usable. Remember: Window = in flight + usable. ACKs move the left edge; window advertisements move the right edge.

## Slide 26
Bandwidth-Delay Product (BDP)
1 Gb/s
Link capacity
80 ms
Round-trip time
10 MB
BDP = bytes that must be in flight to fill the pipe
×153
How much larger than the unscaled 64 KB window
BDP = Capacity × RTT = 10⁹ b/s × 0.08 s = 80 Mb = 10 MB. The receive window (and socket buffers) must be at least the BDP to use the link fully — this requires a window-scale factor of at least 8.
IN403 · Lecture 1 · TCP Deep Dive I
26
Notes: Long fat networks (LFNs) are where tuning matters most. Lab 2 explores this with tc netem. Explanation for students: The bandwidth-delay product is the amount of data that fits “in the pipe” between sender and receiver: link capacity multiplied by round-trip time. To keep a link busy, the sender must have at least one BDP of data in flight at all times; otherwise it will sit idle waiting for ACKs. The BDP grows with both speed and distance. A 10 Mb/s link with a 20 ms RTT has a BDP of only 25 KB, but a 1 Gb/s link across a continent (80 ms) has a BDP of 10 MB — more than 150 times the maximum unscaled TCP window. This is why window scaling exists and why operating systems auto-tune socket buffers. If either the sender’s send buffer or the receiver’s receive buffer is smaller than the BDP, throughput will be limited no matter how much capacity the network has. Such paths are called long fat networks (LFNs).

## Slide 27
Bandwidth-Delay Product (BDP)
EXPLAINED
The bandwidth-delay product is the amount of data that fits “in the pipe” between sender and receiver: link capacity multiplied by round-trip time. To keep a link busy, the sender must have at least one BDP of data in flight at all times; otherwise it will sit idle waiting for ACKs.
The BDP grows with both speed and distance. A 10 Mb/s link with a 20 ms RTT has a BDP of only 25 KB, but a 1 Gb/s link across a continent (80 ms) has a BDP of 10 MB — more than 150 times the maximum unscaled TCP window.
This is why window scaling exists and why operating systems auto-tune socket buffers. If either the sender’s send buffer or the receiver’s receive buffer is smaller than the BDP, throughput will be limited no matter how much capacity the network has. Such paths are called long fat networks (LFNs).
EXAMPLE
1 Gb/s × 0.08 s = 80 000 000 bits = 10 MB. Needed window-scale shift: 10 MB / 64 KB ≈ 153 ⇒ shift of 8 (×256).
REMEMBER
BDP = capacity × RTT. Buffers and windows must be at least the BDP to fill the link.
IN403 · Lecture 1 · TCP Deep Dive I
27
Notes: The bandwidth-delay product is the amount of data that fits “in the pipe” between sender and receiver: link capacity multiplied by round-trip time. To keep a link busy, the sender must have at least one BDP of data in flight at all times; otherwise it will sit idle waiting for ACKs. The BDP grows with both speed and distance. A 10 Mb/s link with a 20 ms RTT has a BDP of only 25 KB, but a 1 Gb/s link across a continent (80 ms) has a BDP of 10 MB — more than 150 times the maximum unscaled TCP window. This is why window scaling exists and why operating systems auto-tune socket buffers. If either the sender’s send buffer or the receiver’s receive buffer is smaller than the BDP, throughput will be limited no matter how much capacity the network has. Such paths are called long fat networks (LFNs). Example: 1 Gb/s × 0.08 s = 80 000 000 bits = 10 MB. Needed window-scale shift: 10 MB / 64 KB ≈ 153 ⇒ shift of 8 (×256). Remember: BDP = capacity × RTT. Buffers and windows must be at least the BDP to fill the link.

## Slide 28
Zero window and the persist timer
What happens
App stops reading → buffer fills
Receiver advertises rwnd = 0
Sender stops sending data
Window update could be lost → deadlock risk
How TCP recovers
Sender starts the persist timer
Sends 1-byte zero-window probes with exponential back-off
Receiver answers with its current window
Wireshark flags: TCP ZeroWindow, ZeroWindowProbe, Window Update
IN403 · Lecture 1 · TCP Deep Dive I
28
Notes: Zero-window events usually indicate a slow application, not a network problem — an important diagnostic distinction. Explanation for students: If the receiving application stops reading (it is busy, blocked or slow), the receive buffer fills up and the receiver advertises rwnd = 0. The sender must then stop sending data entirely. There is a danger here: when the application finally reads data, the receiver sends a window update. That update is a pure ACK with no data, and TCP never retransmits pure ACKs. If it is lost, the sender waits for a window that never comes and the receiver waits for data that never comes — a deadlock. To prevent this the sender starts a persist timer and periodically sends a tiny zero-window probe. The receiver must answer each probe with its current window, so the sender eventually learns that space is available. The probe interval grows exponentially to avoid wasting bandwidth.

## Slide 29
Zero window and the persist timer
EXPLAINED
If the receiving application stops reading (it is busy, blocked or slow), the receive buffer fills up and the receiver advertises rwnd = 0. The sender must then stop sending data entirely.
There is a danger here: when the application finally reads data, the receiver sends a window update. That update is a pure ACK with no data, and TCP never retransmits pure ACKs. If it is lost, the sender waits for a window that never comes and the receiver waits for data that never comes — a deadlock.
To prevent this the sender starts a persist timer and periodically sends a tiny zero-window probe. The receiver must answer each probe with its current window, so the sender eventually learns that space is available. The probe interval grows exponentially to avoid wasting bandwidth.
EXAMPLE
In Wireshark you will see “TCP ZeroWindow” from the receiver, then “TCP ZeroWindowProbe” from the sender every 0.2, 0.4, 0.8 s…, followed by “TCP Window Update” when the application reads again.
REMEMBER
Zero windows point to a slow receiving application, not to network congestion.
IN403 · Lecture 1 · TCP Deep Dive I
29
Notes: If the receiving application stops reading (it is busy, blocked or slow), the receive buffer fills up and the receiver advertises rwnd = 0. The sender must then stop sending data entirely. There is a danger here: when the application finally reads data, the receiver sends a window update. That update is a pure ACK with no data, and TCP never retransmits pure ACKs. If it is lost, the sender waits for a window that never comes and the receiver waits for data that never comes — a deadlock. To prevent this the sender starts a persist timer and periodically sends a tiny zero-window probe. The receiver must answer each probe with its current window, so the sender eventually learns that space is available. The probe interval grows exponentially to avoid wasting bandwidth. Example: In Wireshark you will see “TCP ZeroWindow” from the receiver, then “TCP ZeroWindowProbe” from the sender every 0.2, 0.4, 0.8 s…, followed by “TCP Window Update” when the application reads again. Remember: Zero windows point to a slow receiving application, not to network congestion.

## Slide 30
Silly Window Syndrome and its cures
1
The problem
Tiny windows or tiny writes cause many segments carrying a few bytes each, with a 40-byte header — wasting bandwidth and CPU.
2
Receiver fix (Clark)
Do not advertise a small window increase; wait until the window is ≥ 1 MSS or half the buffer.
3
Sender fix (Nagle)
If unacknowledged data is outstanding, buffer small writes until a full MSS accumulates or an ACK arrives.
4
Nagle + delayed ACK
Combined they can add ~40–200 ms stalls for request/response traffic. Interactive apps set TCP_NODELAY.
IN403 · Lecture 1 · TCP Deep Dive I
30
Notes: A classic production bug: RPC frameworks with 200 ms latency spikes caused by Nagle plus delayed ACKs. Explanation for students: Silly Window Syndrome happens when TCP ends up sending lots of tiny segments. On the receiver side, an application that reads one byte at a time causes the receiver to advertise a one-byte window; on the sender side, an application that writes one byte at a time causes one-byte segments. Each carries 40 bytes of headers, so efficiency collapses. Clark’s rule fixes the receiver side: do not advertise a window increase until it is at least one MSS or half the buffer. Nagle’s algorithm fixes the sender side: while any data is unacknowledged, collect small writes into one segment instead of sending each immediately. Nagle interacts badly with delayed ACKs (receivers wait up to 40–200 ms hoping to piggy-back the ACK on data). A request split into two small writes can then stall until the delayed ACK fires. Latency-sensitive applications (SSH, games, RPC) disable Nagle with the TCP_NODELAY socket option.

## Slide 31
Silly Window Syndrome and its cures
EXPLAINED
Silly Window Syndrome happens when TCP ends up sending lots of tiny segments. On the receiver side, an application that reads one byte at a time causes the receiver to advertise a one-byte window; on the sender side, an application that writes one byte at a time causes one-byte segments. Each carries 40 bytes of headers, so efficiency collapses.
Clark’s rule fixes the receiver side: do not advertise a window increase until it is at least one MSS or half the buffer. Nagle’s algorithm fixes the sender side: while any data is unacknowledged, collect small writes into one segment instead of sending each immediately.
Nagle interacts badly with delayed ACKs (receivers wait up to 40–200 ms hoping to piggy-back the ACK on data). A request split into two small writes can then stall until the delayed ACK fires. Latency-sensitive applications (SSH, games, RPC) disable Nagle with the TCP_NODELAY socket option.
EXAMPLE
Typing in an SSH session sends one keystroke per segment — a 41-byte packet carrying 1 byte of data. With Nagle, keystrokes typed during one RTT are combined into one segment.
REMEMBER
Small writes + Nagle + delayed ACK = mysterious 40–200 ms delays. TCP_NODELAY is the usual fix.
IN403 · Lecture 1 · TCP Deep Dive I
31
Notes: Silly Window Syndrome happens when TCP ends up sending lots of tiny segments. On the receiver side, an application that reads one byte at a time causes the receiver to advertise a one-byte window; on the sender side, an application that writes one byte at a time causes one-byte segments. Each carries 40 bytes of headers, so efficiency collapses. Clark’s rule fixes the receiver side: do not advertise a window increase until it is at least one MSS or half the buffer. Nagle’s algorithm fixes the sender side: while any data is unacknowledged, collect small writes into one segment instead of sending each immediately. Nagle interacts badly with delayed ACKs (receivers wait up to 40–200 ms hoping to piggy-back the ACK on data). A request split into two small writes can then stall until the delayed ACK fires. Latency-sensitive applications (SSH, games, RPC) disable Nagle with the TCP_NODELAY socket option. Example: Typing in an SSH session sends one keystroke per segment — a 41-byte packet carrying 1 byte of data. With Nagle, keystrokes typed during one RTT are combined into one segment. Remember: Small writes + Nagle + delayed ACK = mysterious 40–200 ms delays. TCP_NODELAY is the usual fix.

## Slide 32
Observing flow control on Linux
# Live socket info: rwnd, cwnd, rtt, wscale
ss -tin dst 203.0.113.10
# Receive / send buffer autotuning (min default max)
sysctl net.ipv4.tcp_rmem
sysctl net.ipv4.tcp_wmem
sysctl net.ipv4.tcp_window_scaling
# Raise max buffers for high-BDP paths
sysctl -w net.core.rmem_max=33554432
sysctl -w net.ipv4.tcp_rmem="4096 131072 33554432"
# Wireshark display filter
tcp.analysis.zero_window || tcp.analysis.window_full
ss -i shows wscale, rcv_space, cwnd and rtt for each flow
Linux auto-tunes buffers between min and max
Wireshark’s TCP analysis flags pinpoint window problems
We will practise all of this in Lab 1
IN403 · Lecture 1 · TCP Deep Dive I
32
Notes: Demonstrate live if a Linux VM is available. Explanation for students: Linux exposes the internal state of every TCP connection. The command ss -tin prints, for each socket, the negotiated window scale (wscale), the current congestion window (cwnd), the smoothed RTT (rtt), and how much receive space the kernel has allocated (rcv_space). The tcp_rmem and tcp_wmem settings contain three values: minimum, default and maximum buffer size. The kernel automatically grows buffers between default and maximum as a connection needs them (auto-tuning). If the maximum is smaller than the BDP of your path, auto-tuning cannot help — that is when administrators raise net.core.rmem_max and the third tcp_rmem value. Wireshark adds its own analysis on top of a capture: filters such as tcp.analysis.zero_window or tcp.analysis.window_full find flow-control problems instantly, even in captures with millions of packets.

## Slide 33
Observing flow control on Linux
EXPLAINED
Linux exposes the internal state of every TCP connection. The command ss -tin prints, for each socket, the negotiated window scale (wscale), the current congestion window (cwnd), the smoothed RTT (rtt), and how much receive space the kernel has allocated (rcv_space).
The tcp_rmem and tcp_wmem settings contain three values: minimum, default and maximum buffer size. The kernel automatically grows buffers between default and maximum as a connection needs them (auto-tuning). If the maximum is smaller than the BDP of your path, auto-tuning cannot help — that is when administrators raise net.core.rmem_max and the third tcp_rmem value.
Wireshark adds its own analysis on top of a capture: filters such as tcp.analysis.zero_window or tcp.analysis.window_full find flow-control problems instantly, even in captures with millions of packets.
EXAMPLE
ss -tin output: “wscale:7,7 rtt:48.2/3.1 cwnd:120 rcv_space:262144” ⇒ scaling ×128 both ways, 48 ms RTT, 120 segments in the congestion window, 256 KB receive space.
REMEMBER
Measure before tuning: ss for socket state, sysctl for buffer limits, Wireshark for evidence.
IN403 · Lecture 1 · TCP Deep Dive I
33
Notes: Linux exposes the internal state of every TCP connection. The command ss -tin prints, for each socket, the negotiated window scale (wscale), the current congestion window (cwnd), the smoothed RTT (rtt), and how much receive space the kernel has allocated (rcv_space). The tcp_rmem and tcp_wmem settings contain three values: minimum, default and maximum buffer size. The kernel automatically grows buffers between default and maximum as a connection needs them (auto-tuning). If the maximum is smaller than the BDP of your path, auto-tuning cannot help — that is when administrators raise net.core.rmem_max and the third tcp_rmem value. Wireshark adds its own analysis on top of a capture: filters such as tcp.analysis.zero_window or tcp.analysis.window_full find flow-control problems instantly, even in captures with millions of packets. Example: ss -tin output: “wscale:7,7 rtt:48.2/3.1 cwnd:120 rcv_space:262144” ⇒ scaling ×128 both ways, 48 ms RTT, 120 segments in the congestion window, 256 KB receive space. Remember: Measure before tuning: ss for socket state, sysctl for buffer limits, Wireshark for evidence.

## Slide 34
Window arithmetic
IN-CLASS ACTIVITY · 12 MIN
Work in pairs. Show your calculations.
A path has 500 Mb/s capacity and 40 ms RTT. Compute the BDP in bytes.
What is the smallest window-scale shift that lets a 16-bit window cover this BDP?
Without scaling, what is the maximum achievable throughput on this path?
A receiver advertises rwnd = 0 for 3 s. Sketch the probes the sender emits if the initial persist timeout is 200 ms and doubles each time.
IN403 · Lecture 1 · TCP Deep Dive I
34
Notes: Answers: BDP = 2.5 MB; 2.5 MB / 65 535 ≈ 38.1 → shift 6 (×64) gives 4.19 MB; max ≈ 13.1 Mb/s; probes at ~0.2, 0.6, 1.4, 3.0 s.

## Slide 35
Check your understanding
Q1
Why are TCP sequence numbers byte-based rather than segment-based, and what does the ACK number signify?
Q2
Which options can only be negotiated in the SYN segments, and what happens if a middlebox strips them?
Q3
Explain why the active closer enters TIME_WAIT and why it lasts 2×MSL.
Q4
A transfer peaks at 5 Mb/s on a 1 Gb/s link with 100 ms RTT. What is the most likely cause and the fix?
IN403 · Lecture 1 · TCP Deep Dive I
35
Notes: Give students 2–3 minutes per question in pairs, then discuss answers as a group.

## Slide 36
Model answers
A1
Because TCP is a byte stream: segment boundaries can change on retransmission, but byte positions never do. The ACK number is the next byte the receiver expects; everything before it has arrived.
A2
MSS, Window Scale and SACK-permitted (and Timestamps, which must start in the SYN). If a middlebox strips them, the connection falls back: no scaling (64 KB max window), no SACK, default MSS — often a large performance loss.
A3
TIME_WAIT lets the active closer re-send the last ACK if the peer’s FIN is retransmitted, and ensures old duplicates of this connection expire (2×MSL = maximum lifetime in both directions) before the 4-tuple is reused.
A4
5 Mb/s ≈ 64 KB / 100 ms, so the transfer is window-limited: window scaling is missing or the receive buffer is too small. Fix: enable window scaling end-to-end and raise socket buffer maxima to ≥ BDP (12.5 MB).
IN403 · Lecture 1 · TCP Deep Dive I
36
Notes: Reveal after students have attempted the questions.

## Slide 37
Key takeaways
TCP provides a reliable, ordered, full-duplex byte stream with flow and congestion control
Handshake options (MSS, Window Scale, SACK, Timestamps) shape performance for the whole connection
Flow control limits the sender to the receiver’s advertised window; throughput ≤ window / RTT
High-BDP paths need window scaling and large socket buffers
Zero windows and silly-window effects are usually end-host problems, not network problems
Reading & next session: Kurose & Ross §3.5 (TCP) · RFC 9293, RFC 7323 · Next: Lecture 2 — TCP Congestion Control: Tahoe, Reno & NewReno
IN403 · Lecture 1 · TCP Deep Dive I
37
Notes: Recap the main points and answer final questions.